Chemical Engineering 201

Fall 2005

Group 10

## October 6, 2005

Problem Statement for #4.34(b):

An evaporation-crystallization process of the type described in example 4.5-2 is used to obtain solid potassium sulfate from an aqueous solution of this salt. The fresh feed to the process contains 19.6 wt % K2SO4. The wet filter cake consists of solid K2SO4 crystals and a 40 wt % K2SO4 solution, in a ratio 10 kg crystals/kg solution. The filtrate, also a 40% solution, is recycled to join the fresh feed. Of the water fed to the evaporator, 45.0% is evaporated. The evaporator has a maximum capacity of 175 kg water evaporated/s.

Calculate:

b) The maximum production rate of solid K2SO4, the rate at which fresh feed must be supplied to achieve this production rate, and the ratio kg cycle/kg fresh feed.

| Stream | Total | Water | K2SO4 |
| --- | --- | --- | --- |
| 1 |  |  |  |
| 2 |  |  |  |
| 3 |  |  |  |
| 4 | 175 | 175 | 0 |
| 5 |  |  |  |
| 6 |  |  |  |
| 7 |  | 0 |  |

F7=10*F6

K2SO4				Total

0.196*F1=F7+0.4*F6		F1=F4+F6+F7

0.196*F1=10*F6+0.4*F6		F1=175+F6+10*F6

0.196*F1=10.4*F6		F1=175+11*F6

# 0.196(175+11*F6)=10.4*F6

34.3+2.156*F6=10.4*F6

# F6=4.16 kg

F7=10*4.16=41.6 kg

0.4*F6=F6, K2SO4

F6, K2SO4=1.664 kg

F1=F4+F6+F7=175+41.6+4.16=220.76 kg

0.45*F2, H20=F4=175

F2, H20=388.89 kg

F2, H20=F4, H2O+F5, H2O

388.89=175+ F5, H2O

F5, H2O=213.89 kg

F2=F1+F3

388.89=177.49+F3

F3, H2O=211.4 kg

-6*F3= F3, H2O=211.4

### F2=352.33 kg

# Text boxes

40% K

10 kg solid

1 kg solution

4  45%

6,7

2

1

19.6%K

3

40% K

5

Solution

Solid

Solution:

Max kg/s K2SO4 = 41.6 kg/s

Feed supply rate = 220.76 kg/s

Ratio kg cycle/kg fresh feed = 352.33 kg/220.76 kg = 1.6

Stream

Total

Water

K

2

SO

4

1

220.76

177.49

43.27

2

573.09

388.89

184.236

3

352.33

211.4

140.966

4

175

175

0

5

398.09

213.89

184.236

6

4.16

2.496

1.664

7

41.6

0

41.6