Group 12

Problem 7.5 Felder/Rousseau

Air at 300 ˚C and 130 kPa flows through a horizontal 7- cm ID pipe at velocity of 42.0 m/s.

- Calculate  (W), assuming ideal gas behavior

- If the air is heated to 400 ˚C at constant pressure, what is

Δ Ek =  Ek(400 ˚C) – Ek (300˚C)?

- Why would it be incorrect to say that the rate of transfer of heat to 		the gas in part (b) must equal the rate of change of kinetic energy?

Helpful equations

1)	, m = mass, u = velocity (m/s)

2)

Standard Conditions for Gases

| System | Ts | Ps | Vs | ns |
| --- | --- | --- | --- | --- |
| SI | 273K | 1 atm | .002415 m3 | 1 mol |
| CGS | 273K | 1 atm | 22.415 L | 1 mol |

(a)

Find volumetric flow rate

= velocity x Area:	= 161.635 L/s

Find molar flow rate (rearrange and use equation 2)

Find mass flow rate

113 J/s

(b) Follow along with the Presenter