Group 4

Methane reacts with chlorine to produce methyl chloride and hydrogen chloride.  Once formed, the methyl chloride may undergo further chlorination to form methylene chloride (CH2Cl2).

A methyl chloride production process consists of a reactor, a condenser, a distillation column, and an absorption column.  A gas stream containing 80.0 mole % methane and the balance chlorine is fed to the reactor.  In the reactor a single- pass 100% chlorine conversion is attained, the mole ratio of methyl chloride to methylene chloride in the product is 5:1.  The product stream flows to a condenser.  Two streams emerge from the condenser, the liquid condensate, which contains all of the methyl chloride and methylene chloride in the reactor effluent, and a gas containing the methane and hydrogen chloride. The condensate goes to the distillation column in which the two component species are separated.  The gas leaving the condenser flows to the absorption column where it contacts an aqueous solution.  The solution absorbs all of the HCl and none of the CH4 in the feed.  The liquid leaving the absorber is pumped elsewhere in the plate for further processing, and the methane is recycled to join the fresh feed to the process (a mixture of methane and chlorine). The combined stream is the feed to the reactor.

What molar flow rates and compositions of the fresh feed and the recycle stream are required to achieve a methyl chloride production rate of 1000 kg/hr?

ζ1

CH4 + Cl2 ( CH3Cl + HCl

ζ2

CH3Cl + Cl2 ( CH2Cl2 + HCl

Are not significantly formed

CH2Cl2 + Cl2 ( CHCl3 + HCl

CHCl3 + Cl2 ( CCl4 + HCl

| Streams | CH4 | Cl2 | CH3Cl | HCl | CH2Cl2 |
| --- | --- | --- | --- | --- | --- |
| 1 |  |  |  |  |  |
| 2 |  |  |  |  |  |
| 3 |  |  |  |  |  |
| 4 |  |  |  |  |  |
| 5 |  |  |  |  |  |
| 6 | 0 | 0 | 0 | 0 | 3960 |
| 7 | 0 | 0 | 19800 | 0 | 0 |
| 8 |  |  |  |  |  |
| 9 |  |  |  |  |  |
| 10 |  |  |  |  |  |

Write ζ equations

In 		-out 		+produced	-consumed	= accumulated

CH4 :          F2,CH4  	______ 	+ 0   		-  ζ1 		= 0

Cl2 : 	       ______	-0 		+ 0 		______  	= 0

CH3Cl :       0		- F3, CH3Cl 	______	- ζ2 		= 0

HCl :           0 		______ 	______	- 0 		= 0

CH2Cl2 :     ______	- F3,CH2Cl2 	+ ζ2 		______	= 0

Look at the ζ equations and check what we know.

We see can solve for ζ2

F3,CH2Cl2 = ζ2

______  = ζ2

Now go back to ζ equations and see that we can solve for _____

______ = F3, CH3Cl  +  ζ2

Return to ζ equations we can now solve for ______ and ______

______ = ζ1  + ζ2

______ = ζ1  + ζ2

Go back to the ζ equations we seem to be stuck, we aren’t! Pay attention to see the dramatic conclusion.

# Text boxes

Distiller

Reactor

Condenser

Absorption

Column

1

2

0 .80 mol CH4

0 .20 mol Cl2

10

3

5

6

7

9

8