Group 9

Problem 6.1

Ten mL of pure liquid water in a cylinder with a movable piston is heated at a constant pressure of 1 atm from an initial temperature of 80°C. The temperature of the system is monitored, and the following behavior is observed:

- What is happening in steps AB, BC, and CD? What is the temperature corresponding to the horizontal portion of the curve?

- Estimate the volume occupied by the water at points B and C. (Assume the vapor follows the ideal gas equation of state.)

Solution:

Part a:

AB ( heating liquid

BC ( phase change  (100°C)

CD ( heating gas

Part b:

B: H2O liquid:

= 0.01 L H2O

C: H2O gas

PV = nRT

n:   0.556 mol H2O

T:  80°C + 273 = 353 K

V = 16.1 L H2O