Problem 2.9

This is another problem where we have to do some unit conversion and figure out what the problem statement is telling us to do.

Problem statement:  A waste treatment pond is 50 m long and 15 m wide, and has an average depth of 2 m.  The density of the waste is 85.3 lbm/ft3.  Calculate the weight of the pond contents in lbf.

Solution:  I read the problem to get a general idea what it was all about.

I read the problem again and the following data was given:

a pond is 50 m long and 15 m wide and has a depth of 2 m.  Density of a waste is 85.3 lbm/ft3.

I drew a sketch:

Calculate weight of the pond in lbf.

I calculated the total volume of the pond:

L = 50 m

W = 15 m

D = 2 m

V = LWD = (50)(15)(2) = 1500 m3

I converted this to ft3:

1500 m3 (35.3145 ft3/m3) = 52971.75 ft3.

Then, I multiplied this volume by the density of the waste in order to get rid of ft3:

(85.3 lbm/ft3)(52971.75 ft3) = 4518490.27 lbm.

Finally, I do another unit conversion because there are 1lbm / 1lb f:

Weight of water = 4518490.27 lbf.

# Text boxes

50m

15 m

2 m