## Slide 1: Verifying ADS-B Navigation Information Through Doppler Shift Measurements
Nirnimesh Ghose and Loukas Lazos
Department of Electrical and Computer Engineering,
University of Arizona
Presented at:
34th Digital Avionics Systems Conference, Prague

## Slide 2: Air Traffic Growth
Air traffic continues to grow to unprecedented volume
NextGen system is expected to modernize air traffic management and cope with congestion, safety, and cost

## Slide 3: Migration from Radar to NextGen
Radar system
Automatic Dependent Surveillance – Broadcast
(ADS-B)
Uncooperative
Independent analogue system
Ground station dependent
Expensive to deploy and maintain
Coarse navigation information
Cooperative
Dependent digital system
Aircraft-to-aircraft communications
Cheaper to deploy and maintain
Fine-grained navigation information

## Slide 4: ADS-B Architecture
Air Traffic Controller
ADS-B Out
ADS-B In
ADS-B Out
Location from GPS
Location from GPS
Navigation Information:
Location, Speed, Heading etc.

## Slide 5: ADS-B Frame Format
DF: Downlink Format
CA: Message Subtype
AA: ICAO aircraft address
ME: Data frame
FI: Flight Identification Pos: Position PI: Position Integrity BGA: Barometric and geometric Altitude VR: Vertical Rate
TAGS: Track Angle and Ground Speed EI: Emergency Indication SPI: Special Position Indication
PI: Parity check

## Slide 6: (In)Security of ADS-B
ADS-B standard does not provision for secure communications
  No sender authentication
  No message integrity
  Weak location verification between aircraft and ground stations
Numerous vulnerabilities have been demonstrated
  Costin and Francillon [1] experimentally demonstrated eavesdropping, message injection, replaying, jamming, using a USRP and COTS components
  Sampigethaya et al. [2] have enumerated eavesdropping, jamming, aircraft impersonation, active manipulation of data, and others.
  Krozel et al. [3] have proposed the use of intent conformance and geometric conformance to verify the integrity of ADS-B signals
  [1] Costin, Andrei, and Aurélien Francillon. "Ghost in the Air (Traffic): On insecurity of ADS-B protocol and practical attacks on ADS-B devices." Black Hat, USA
  (2012).
  [2] Sampigethaya, Krishna, et al. "Future e-enabled aircraft communications and security: The next 20 years and beyond." Proc. of the IEEE 99.11 (2011):
  2040-2055.
  [3] Krozel, Jimmy, et al. "Aircraft ADS-B Data Integrity Check." Proc. of the AIAA Aviation, Technology, Integration, and Operations Conference (2004).

## Slide 7: Fundamental Security Problems in ADS-B
Air Traffic Controller
ADS-B Out
ADS-B In
ADS-B Out
Sender Authentication (point-to-point, broadcast)
Message Integrity
Freshness
Resistance to Jamming
Crypto solutions readily available

## Slide 8: ADS-B Security using Classic Cryptography
Strohmeier, Martin, Vincent Lenders, and Ivan Martinovic. "Security of ADS-B: State of the Art and Beyond." arXiv preprint (2013).
Requires worldwide key management
  Key establishment, revocation, refresh, certificate management, etc.
Requires substantial revision of the existing standard
Can we verify ADS-B broadcasts
without crypto?

## Slide 9: Our Contributions
We propose a PHY-layer based mechanism for verifying the integrity of ADS-B navigation information without modifying the ADS-B standard
Verification of the aircraft’s position and velocity, by exploiting the Doppler spread phenomenon
Malicious ground station cannot spoof a “ghost" aircraft by transmitting ADS-B frames containing rogue navigation vectors
Defeating our verification method is equivalent to forging signatures in unbalanced oil and vinegar signature schemes

## Slide 10: Problem Statement
Rogue transmitter G
A
B
Spoofed Trajectory
Navigation Information:
nX = {lX, vX}
Position
nB= {lB, vB}
nA = {lA, vA}
Velocity
Verify navigation information from an aircraft

## Slide 11: Velocity and Position Verification
Velocity and position are inter-connected via Kinematic equations
Doppler spread is calculated from velocity and carrier frequency

## Slide 12: Maximum Doppler Spread Estimation
A
B
Estimate Doppler Spread
*Tepedelenlioğlu, Cihan, and Georgios B. Giannakis. "On velocity estimation and correlation properties of narrow-band mobile communication channels.“ Vehicular Technology, IEEE Transactions on 50.4 (2001): 1039-1052.
We estimate the Doppler spread using channel correlation measurements [Tepedelenlioglu and Giannakis, 2001]*
Based on averaging M+1 samples

## Slide 13: Verification Process: Step 1
A
B
Claimed Trajectory
1
2
…
k
Claimed location and velocity vectors received by verifier (A)

## Slide 14: Verification Process: Step 2
A
B
Claimed Trajectory
1
2
…
k
Claimed heading estimated by the verifier (A)

## Slide 15: Verification Process: Step 3
A
B
Claimed Trajectory
1
2
…
k
Velocity of prover (B) estimated from Doppler spread by verifier (A)

## Slide 16: Verification Process: Step 4
A
B
Claimed Trajectory
1
2
…
k
Estimated and claimed distance covered by prover (B) in inter-frame time (tP)

## Slide 17: Verification Process: Step 5
A
B
Claimed Trajectory
1
2
…
k
RMSE for velocity and location estimated by verifier (A)

## Slide 18: Security Analysis: Spoofing a Desired Trajectory
A
B
Claimed Trajectory
lB(1)
lB(2)
…
lB(k)
Rogue transmitter G
vB|A(1)
vB|A(2)
…
vB|A(k)
ωD(1)
ωD(2)
…
ωD(k)
hGA
hBA
nA = {lA, vA}
preamble

## Slide 19: Security Analysis: Spoofing a Desired Trajectory
Equivalent to an “Oil” and “Vinegar” signature scheme [ Kipnis et al.]
M’ “oil” variables and αNS - M’ “vinegar” variables
TS symbol duration
T sampling period
Kipnis, Aviad, Jacques Patarin, and Louis Goubin. "Unbalanced oil and vinegar signature schemes." Advances in Cryptology—EUROCRYPT’99. Springer Berlin Heidelberg, 1999.
S, has many solutions Ψ due to underdefined nature of equation system
To spoof ωDsp, the rogue ground station needs to have a whole solution set

## Slide 20: Security Analysis: Shifting the Central Frequency
For ADS-B scenario with fc = 1090MHz and frequency offset upto 312.5KHz
Change in radial velocity is up to 0.03%

## Slide 21: Security Analysis: Alt Trajectory for Max Doppler Spread

## Slide 22: Evaluation: Simulation Setup
Two aircrafts model cruising at constant velocity of 900km/h
Symbol duration (TS ) of 10-6 sec
A Rician channel with K-factor of 50 (LoS communication)
Doppler spectrum is simulated using Jake’s model
ADS-B preamble set to 8 symbols (NS = 8), with a sampling period (T = 5 * 10-8 sec)
This gives us 16 equations with 16 “oil” variables and 134 “vinegar” variables

## Slide 23: Evaluation: Scenario 1
Aircraft B proves its true trajectory to aircraft A
Distance between the aircrafts varies linearly from 130Km to 80Km which varies the number of captured frames (k) and record RMSEv and RMSEl

## Slide 24: Evaluation: Scenario 1
Aircraft B proves its true trajectory to aircraft A
Distance between the aircrafts varies linearly from 130Km to 80Km which varies the SNR and record RMSEv and RMSEl

## Slide 25: Evaluation: Scenario 2
A rogue ground station G spoofing a ghost aircraft B at aircraft A
Probability of success is measured for different values of captured frames (k)

## Slide 26: Conclusion and Future Work
We proposed and PHY-layer navigation information verification scheme for ADS-B
  An aircraft can verify the location and velocity of another aircraft
  Exploited the Doppler spread to measure velocity
  Showed that emulating a ghost aircraft is equivalent to solving underdefined quadratic equation system
Future Work:
Collusion of multiple ground stations to spoof a “ghost” aircraft
Emulates of a “ghost” aircraft by an airborne attacker
Verification in other flight phases such as takeoff and landing

## Slide 27: Thank you!